## Slide 1: Smart street lighting system
Team:- N.Abhiram (1602-20-737-121)
D.Kiran (1602-20-737-139)
K.Saketh (1602-20-737-165)

## Slide 2: SIH 2022 PS DETAILS
Problem statement : An automated feedback system to know the exact location of non-functional street lights in rural/urban areas of India . Also automatic turning on & off according to the surroundings.
PS No : ST888
Thrust Area : Miscellaneous

## Slide 3: TABLE OF CONTENTS 01 02 03 04
ABSTRACT
Description about project
Use case paradigm
Technologies used
05
Test cases

## Slide 4: ABSTRACT
Good Street lighting systems in rural areas improve road safety, personal security and raise the standard of living. Street lighting also improves safety for drivers, riders, and pedestrians on roads, where the road conditions are sometimes not of the desired standards. Streetlights have been installed in many villages and state highways in Central India. However, many times these lights remain non- functional due to late information about the exact location and unavailability of sufficient service support. Consequently, in the absence of proper lighting, some of these areas become unsafe for people at night especially elders, women, and children. An automated feedback system based on a software may allow the service engineers to know the exact location of non-functional streetlights in their areas of responsibility. And also to ensure maximum efficiency and energy saving purpose a system is also designed in such a way that light is switched on or off depending upon its environment.

## Slide 5: DESCRIPTON ABOUT PROJECT
We tend find the street lights which are not working properly (faulty) through a LDR(photoresistor) that placed under the street light.
The Arduino is coded in such a way that the emitting light intensity is calculated and if the calculated value is less than the required lux value that is 10 then Arduino triggers a signal.
This signal is moved to Ublox module where the geographical location consisting of latitude and longitude are taken.
The data about geographical location and time stamp is transmitted to the webserver using
WIFI module(ESP 8266).
These latitude and longitude values are then decoded into a real time location using GeoPy module present in python.
The time stamp and geographical location are stored in the webserver and we trigger a request to the service operator present in the nearby area.
The service operator receives a request when there is fault detected and when the request is completed the service operator resets the device.

## Slide 6: DESCRIPTON ABOUT PROJECT
Also the street lights are equipped with IR (Infrared ) sensors which is capable of detecting any kind of motion .
The motion detected is then considered as an input and the light is set to high meaning light is ON.
The LDR is again used to detect the light intensity after the IR sensors input and light ON as output.
This confirms whether the light is properly working or is it faulty.
Another feature is that the lights are automatically tend to ON or OFF based on the LDR input. Here the input is taken from the environment that Is whether is it sunny or night outside.

## Slide 7: USE CASE PARADIGM
l

## Slide 8: TECHNOLOGIES USED
Hardware :-
            Arduino Uno
            Ublox Neo – 6M
            LDR
            ESP 8266
            IR Sensor
            Software:-
            HTML,CSS and PHP
            MYSQL
            Python GeoPy
            ARDUINO IDE

## Slide 9: Program Flow Chart-I
l
Setup() :-

## Slide 10: Program Flow Chart-II
l
Loop() :-

## Slide 11: IOT SYSTEM CIRCUIT DESIGN

## Slide 12: TEST CASES
Case 1
Description:- The LDR sensor should detect the high intensity of light meaning it is day outside.
Pre-condition :- LDR lux value should be less than 900 units.
Expected output :- The system should display the condition and the lux value.
OUTPUT SCENARIO :-

## Slide 13: TEST CASES(cont..)
Case 2
Description:- The LDR sensor should detect the low intensity of light and should identify any object.
Pre-condition :- LDR lux value should be more than 900 units and no motion is detected.
Expected output :- The system should display the lux value and motion status.
OUTPUT SCENARIO :-

## Slide 14: TEST CASES(cont..)
Case 2.1
Description:- The LDR sensor should detect the low intensity of light and should identify any object.
Pre-condition :- LDR lux value should be less than 900 units and the motion is detected.
Expected output :- The system should turn the LED on and LED should be at maximum brightness.
OUTPUT SCENARIO :-

## Slide 15: TEST CASES(cont..)
Case 3:
Description:- The LDR sensor should detect the Low intensity of light and one IR sensor should detect the motion and the street light is faulty.
Pre-condition :- LDR lux value should be less than 900 units and the IR sensor should detect motion. Also the second LDR should detect the faulty street light.
Expected output :- The system should send the geographical location to the webserver.
OUTPUT SCENARIO :-

## Slide 16: TEST CASES(cont..)
Case 3:
OUTPUT SCENARIO :-

## Slide 17: REFERENCES
            https://thesai.org/Downloads/Volume11No8/Paper_53-IoT_Based_Automatic_Damaged_Street_Light.pdf
            https://nevonprojects.com/iot-streetlight-controller-system/
            https://ijesc.org/upload/1eb3edd88907de6c42cde91d7245908f.Intelligent%20Street-Light%20System%20using%20Arduino%20UNO.pdf
            https://www.researchgate.net/publication/348096383_Smart_Street_Lighting_System